## Slide 1: Game AI (Game Engines 2)
Dr Bryan Duggan
Dublin Institute of Technology

## Slide 2: What we will learn today
Unity basics
The framework code for the examples on this course
Implementing steering behaviours in Unity

## Slide 3
Unity is an platform for making games
Features
  Game engine
  Scene editor
  3D or 2D Games
  GameObjects, GameComponents
  PhysX and Box2D physics
  Class library
  Bindings for C#, Boo and JavaScript
  Uses MONO (Open Source .Net)
  Runtimes for PC, Mac, Linux, IOS, Android etc etc.

## Slide 4: In industry
Huge presence at GDC
Very popular amongst indies
Free & Pro versions
  Free for games up to 100K
  Pro version has a few extra features
  Including Rift support
  Pro version is expensive
  75 Euro PM

## Slide 6: Concepts
GameObject
  Represents anything in the scene
  Has a Transform object
  Does not draw itself! (Thats what a GameComponent is for)
  Can contain other GameComponents
  Can be attached to other GameObject’s
    Parent’s transform is multiplied into the child’s
  You rarely extend GameObject
GameComponent
  Contained by a GameObject (GameObject’s can have multiple GameComponents attached)
  Start – Called at the start of the lifetime
  Update – Called once per frame
  Use Time.deltaTime to get the time delta

## Slide 7: Concepts
Transform
  Contains forward, up and right vectors
  A quaternion called rotation
  A position vector
  Probably has a world transform, but its not visible?
  This is the object that controls the GameObject’s world transform
Renderer
  A subclass of GameComponent
  There are lots of subclasses for different types of drawable object

## Slide 8: Useful Classes
Vector3
  x, y, z fields (lowercase)
  +, -, * / overloaded
  magnitude (lowercase)
  Dot, Cross, Normalize (static methods)
  Use the static fields forward, right and up to get the basis vectors
Quaternion
  w, x, y, z fields (lowercase)
  * is overloaded for quaternions and vectors
  * a vector rotates the vector by the quaternion
  Use:
    Quaternion q = Quaternion.AngleAxis(90, Vector3.up);
    To make one!
    Angle is in degrees

## Slide 9: Matrix operations
Are not supported!
Instead use a quaternion for rotations and
Transform object for everything else (including rotations)
E.g:
  Vector3 target = Vector3.zero;
  target = leader.transform.TransformPoint(offset);
  To transform a point by the transform
  Also:
    TransformDirection
    InverseTransformDirection
    InverseTransformPoint

## Slide 10: Creating GameObjects in code..
Create a “prefab” (a game object with some components attached)
This is done automatically when you import a model
Create a public field in the game component
  This exposes the field to the Unity editor
Drag the prefab over to the field in the editor
Write code:
  boid = (GameObject) GameObject.Instantiate(prefab);
  boid.tag = "boid";
  boid.AddComponent<SteeringBehaviours>();
  boid.transform.position = position;

## Slide 11: Referencing other GameObjects/GameComponents
Use the tag to assign a string tag to the object
Use:
  GameObject[] obstacles = GameObject.FindGameObjectsWithTag("obstacle");
  GameObject obstacles = GameObject.FindGameObjectWithTag("obstacle");
Use:
  leader.GetComponent<SteeringBehaviours>()
  To get a component of a GameObject

## Slide 12: Debugging C# Code
Can’t use VisualStudio without an expensive plugin
Instead use MonoDevelop
The .sln .csproj files get regenerated each time you build your project
Add these to your .gitignore file
Set breakpoints etc in MonoDevelop
Choose Run | Attach to Process in MonoDevelop
Unity must be already running but not running your project
Run the project in Unity

## Slide 13: My Game AI Framework!

## Slide 14: Main Classes
SteeringBehaviours
  A GameComponent
  Implements all the behaviours!
  You must call Params.Load before using
  Uses bit masking to control which behaviours are turned on
  Has properties that are exposed in Unity
SteeringManager
  A singleton
  Attached to a GameObject with no renderer
  Used to control which scenario is run
  Displays the HUD
  Handles turning on and off various display settings
  Exposes the prefabs required by the scenarios
  Should not be necessary if you are using the Unity editor to create scenes

## Slide 15: Main Classes
Scenario
  Base class for each of the demos
  Has Setup, Update and TearDown methods
  Handles mouse clicks to move the targetPos of the behaviours
  leader is a special game object
  TearDown removes all the objects from the scene
Special tags!
  “boid”, “obstacle”, “MainCamera”

## Slide 16: Subclasses
SeekScenario
ArriveScenario
PursueScenario
StateMachineScenario
PathFollowingScenario
PathFindingScenario
ObstacleAvoidanceScenario

## Slide 17: Bitmasking
Allows you to store lots of booleans in a single int value
First create a mask with the bit you want
  int mask = 1 << 5
Operations
  Set a bit
    OR with the mask
  Clear a bit
    AND with the inverse of the mask
  Toggle a bit
    XOR with the mask
  Read a bit
    AND with the mask and check for non zero

## Slide 18: In code:
public bool isOn(behaviour_type behaviour)
{
return ((flags & (int)behaviour) == (int)behaviour);
}
public void turnOn(behaviour_type behaviour)
{
flags |= ((int)behaviour);
}
public void turnOff(behaviour_type behaviour)
{
flags &= ( ~ (int)behaviour);
}

## Slide 19: Offset pursuit (3D)
Used to program fleets (amongst other things)
Similar to pursue but with 2 differences
  The agent pursues an offset (in local space) of the target agent
  Transform the offset by the target agents Transform object to get the target
  Use dead reckoning same as pursue
  We use arrive instead of seek to keek in formation

## Slide 20: Code...
Vector3 OffsetPursuit(Vector3 offset)
{
Vector3 target = Vector3.zero;
target = leader.transform.TransformPoint(offset);
float dist = (target - transform.position).magnitude;
float lookAhead = (dist / Params.GetFloat("max_speed"));
target = target + (lookAhead * leader.GetComponent<SteeringBehaviours>().velocity);
checkNaN(target);
return Arrive(target);
}

## Slide 21: Wall Avoidance (3D)
Uses “feelers”
  Points projected in front of the agent
  3 for 2D 5 for 3D
  Make them in local space
  Use the forward basis vector and a quaternion to make them
  Transform to world space
  Can use Plane geometry to check the points

## Slide 22: In code...
Vector3 newFeeler = Vector3.forward * feelerDistance;
newFeeler = transform.TransformPoint(newFeeler);
Feelers.Add(newFeeler);
newFeeler = Vector3.forward * feelerDistance;
newFeeler = Quaternion.AngleAxis(45, Vector3.up) * newFeeler;
newFeeler = transform.TransformPoint(newFeeler);
Feelers.Add(newFeeler);
newFeeler = Vector3.forward * feelerDistance;
newFeeler = Quaternion.AngleAxis(-45, Vector3.up) * newFeeler;
newFeeler = transform.TransformPoint(newFeeler);
Feelers.Add(newFeeler);
newFeeler = Vector3.forward * feelerDistance;
newFeeler = Quaternion.AngleAxis(45, Vector3.right) * newFeeler;
newFeeler = transform.TransformPoint(newFeeler);
Feelers.Add(newFeeler);
newFeeler = Vector3.forward * feelerDistance;
newFeeler = Quaternion.AngleAxis(-45, Vector3.right) * newFeeler;
newFeeler = transform.TransformPoint(newFeeler);
Feelers.Add(newFeeler);

## Slide 23: Planes
Can be described using a point on the plane and a normal vector, a vector perpendicular to the plane

## Slide 24: Equation of a plane
Remember
Cos(90) = 0, so
If A and B are perpendicular vectors: A.B = 0
The equation of a plane is given by
  n.(p – p0) = 0

## Slide 25: Equation of a plane
n.(p-p0) Can be written as:
n.p –n.p0 (Distributive)
We can therefore write the equation as: n.p + d = 0 Where d = -n.p0
d is also shortest signed distance from the origin to the plane
A plane is 4 values A, B, C and D
A, B, C are the normal
D is the shortest signed distance to the plane

## Slide 26: Planes in Unity